## Slide 1: Thrombin Time :
It does not test for deficiencies in the extrinsic or intrinsic pathway , it only measures the availability of functional fibrinogen . So it bypasses the prior steps in the coag cascade , only fibrinogen (thrombin) fibrin
So it is affected by levels of fibrinogen < 100 mg/dL ,
4/5/2011
1

## Slide 2
dysfibrinoginemia and circulating antithrombin , heparin ,plasmin , FDPs
It is a sensitive test in detecting heparin and presence of DIC
normally it is prolonged in the new born, multiple myeloma ( the abnormal globulin interferes with the polymerization of fibrin )
4/5/2011
2

## Slide 3
Principle :
An amount of thrombin is added to plasma and the length of the time required for clot to form is measured , report as T.T in sec
normal range : 15 to 20 sec.
4/5/2011
3

## Slide 4
Procedure :
1. 0.1 ml of working TRIS buffer , prewarm at 37 ◦c for 3 min (not > 10 min).
2. Add 0.1 ml of patient plasma , incubate at 37◦ C at exactly 1 min , add 0.1 ml of thrombin reagent , measure the clotting time
If prolonged :
dilute 1:1 with normal plasma→
if T.T = control →deficiency or molecular abnormality of fibrinogen;
If not corrected → presence of a circulating inhibitor ( or heparin)

## Slide 5: Reptilase Time
Reptilase is an enzyme found in the
venom of the Bothrops Atrox Snake . It is
capable of converting fibrinogen to fibrin
by hydrolyzing FPA +AP only from fibrinogen .
it is not affected by heparin (the clot formed is more fragile than that formed by thrombin ) .
so it is helpful in testing for fibrinogen in patient receiving heparin .(minimum effect of heparin on repilase ) .
It is prolonged if FDPs are present .
Normal :18- 25 sec
Reagent Atroxin = Reptilase
4/5/2011
5

## Slide 6
NOTES :
If a patient is receiving heparin will generally show prolonged T T but normal Reptilase time
FDPs in a conc of 40 ug/dl or higher give prolonged Reptilase time
Hypofibrinogenemia or Dysfibrinogenemia + Afibrinogenemia + streptokinase therapy will result in prolonged both TT and Reptilase time
If TT is prolonged while slight to mod inc Reptilase , indicate FDPs presence
.4/5/2011
6

## Slide 7
principle :
when Atroxin (Reptilase ) is added to plasma it releases FPA from the fibrinogen molecule , monomers polymerize to form clot

## Slide 8: FXIII screening test : Urea Solubility test
It is responsible for converting the fibrin clot to more stable form , it is activated by thrombin during the fibrinogen - fibrin conversion .
FXIII causes the formation of covalent bonds between the fibrin monomers , thus stabilizing the fibrin polymer
When F XIIIa is present, the fibrin clot formed is insoluble in 5 M urea ( or 1% monochloroacitic acid or 2% acetic acid) When left standing for 24 hr .
4/5/2011
8

## Slide 9
A deficiency of this factor is rare
Generally , 1% level of F XIII is sufficient to make a clot insoluble in 5 M Urea.
Principle:
Patient’s plasma is clotted by the addition of CaCl2 . Urea is added to the clot , if FXIII is absent  clot is dissolved in less than 24 hr .
4/5/2011
9

## Slide 10
Procedure :
1. 0.2ml of plasma + 0.2 ml of 0.025 M CaCl2 , mix , incubate at 37 ◦c for 30 min (patient & control)
2. Loosen the clot from the sides of the test tube by gently tapping the sides of the tube
3.Transfer the patient’s clot to a tube containing 5 ml of Urea.
4. Transfer both of the patient’s + control clots to another tube containing urea
4/5/2011
10

## Slide 11
5. Incubate at room temp for 24 hr , examine and note if the clot is dissolved Report the length of time it took the patient’s clot to dissolve.
If not dissolved after 24 hrs.report insoluble after 24 hr.
If dissolved before 24 hr .- FXIII is less than 2%of the normal
In this case patient’s mixed control clot should not dissolve.
If it does dissolve indicate a fibrinolytic process rather than F XIIIdef.
If FXIII is deficient  clot dissolves within 2-3 hrs
4/5/2011
11